Water quality (Data table, Map, Site-info table) Winn’s Brook and Wellington Brook in Belmont

— collected by the Mystic River Watershed Association March 28 2006

Data

Winn's Brook & Wellington Brook in Belmont & Cambridge, Hotspot Sampling March 28, 2006. Dry weather. Air temp 0 to 11.0 C

Monitors:  Jenny Birnbaum & Steve Murphy

Definitions of terms in column headings

- cfu (in E. coli cfu/100mL) = colony forming units per 100 milliliters  (is a unit of measurement for bacteria)

- DO %sat = percent saturation  (is a unit of measurement for dissolved oxygen)

- DO (in DO mg/l) = milligrams per liter (is a unit of measurement for dissolved oxygen)

- us/cm (in Sp. Cond. us/cm) = microsiemens per centimeter (a unit of measurement for specific conductivity, which is conductivity standardized to a temperature of 25 degrees Celsius; specific conductivity is also called temperature corrected conductivity)

| Sample # | Site ID | E. coli cfu/100mL | H2O Temp. C | DO %sat | DO mg/l | Sp. Cond. us/cm | Time am | Town | Type | Site Description [and Comments] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1241 | WIB001 | 780 | 6.7 | 95 | 11.58 | 494 | 6:15 | Belmont | centerline | Winn's Br. outflow to Little Pond- park on Larch Circle- walk down path between 145 & 163 Brighton- sample left side of bridge |
| 1242 | WIB005 | 2069 |  |  |  |  | 6:37 | Belmont | centerline | Brook covered here- grate over Winn's Br on N side of Sherman St. E of Broad St. |
| 1243 | WIB009 | 97 | 4.9 | 96.9 | 12.38 | 450 | 6:48 | Belmont | centerline | Winn's Br beside 73 Claflin St. US of grate |
| 1244 | WIB012 | 21 | 5.1 | 96.6 | 12.28 | 433 | 7:01 | Belmont | centerline | Winn's Br on E side of Clifton St by Hickory Lane |
| 1245 | WIB013 | 16 | 5.2 | 94.5 | 12 | 420 | 7:10 | Belmont | centerline | Winn's Br @ Howells Rd footpath bridge- park on Fletcher & walk up driveway of blue house [Comment: DS side] |
| 1246 | WIBUTB | 8 |  |  |  |  | 7:24 | Belmont | tributary | Tributary 'B' to Winn's Br on S side of Prospect St W of Clifton- park on Prentiss |
| 1247 | WIB018 | 236 | 8.2 | 91.9 | 10.79 | 487 | 7:38 | Belmont | centerline | Winn's Br @ Juniper Rd [Comment: DS side, long green algae] |
| 1248 | ATB007 | 123 |  |  |  |  | 7:50 | Belmont | centerline | Atkins Br @ Somerset St (near Habitat sanctuary) |
| 1249 | WEB013 | 38730 | 10.1 | 87.5 | 9.81 | 1,037 | 8:09 | Belmont | centerline | Wellington Brook emerging from under Common Street- park on Dunbarton Rd |
| 1250 | WEB010 | 5654 | 9.6 | 113.6 | 12.87 | 1,012 | 8:22 | Belmont | centerline | Wellington Brook behind E end of library where brook goes back underground |
| 1251 | WEB007 | 4480 | 8.2 | 102.8 | 11.87 | 1,024 | 8:42 | Belmont | centerline | Wellington Brook inflow to Claypit Pond @ SW corner by Concord Ave. |
| 1252 | BEL08N | 205 | 6.6 | 99.2 | 12.07 | 1,422 | 8:59 | Belmont | pipe | North (& side) pipe of two circular pipes- inflow to Blair Pond where Wellington Br emerges fr Blanchard Rd/Brighton St [Comment: pipe on inside not flowing] |
| 1253 | CAMD34 | 1379 | 8.6 | 66.5 | 8.05 | 694 | 9:03 | Cambridge | pipe | South, rectangular outfall- inflow to Blair Pond where Wellington Br emerges fr Blanchard Rd/Brighton St [Comment: pipe on inside not flowing] |
| 1254 | WEB002 | 148 | 7.9 | 100.5 | 11.86 | 1,423 | 9:18 | Belmont/ Cambridge | centerline | Blair Pond outlet on N side just before R/R- becomes Wellington Br.- park on Flanders Rd. |

Map

- All maps are from digital orthophotos

- courtesy of Office of Geographic and Environmental Information (MassGIS), Commonwealth of Massachusetts Executive Office of Environmental Affairs

- sites colored in green had E. coli concentrations below the state swimming standard of 200cfu/100ml for fecal coliforms

- sites in red were above the 1000cfu/100ml standard for secondary contact,

- and those between 200 and 999 are in yellow

- Add 1000 to site numbers on maps to get site ID's on "data" worksheet.

Winn's Brook & Wellington Brook (Belmont/Cambridge)

Site Info

MyRWA Sample  Monitors:  Jenny Birnbaum & Steve Murphy 2006

| MyRWA Site | EPA Sample | Town | Date | N Degr | N Min | N Sec | W Degr | W Min | W Sec | Type | Directions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| WIB001 | 1241 | Belmont | 0328 | 42 | 23 | 57.28 | 71 | 9 | 39.66 | centerline | Winn's Br. outflow to Little Pond- park on Larch Circle- walk down path between 145 & 163 Brighton- sample left side of bridge |
| WIB005 | 1242 | Belmont | 0328 | 42 | 23 | 53.71 | 71 | 10 | 0.37 | centerline | Brook covered here- grate over Winn's Br on N side of Sherman St. E of Broad St. |
| WIB009 | 1243 | Belmont | 0328 | 42 | 23 | 56.68 | 71 | 10 | 23.37 | centerline | Winn's Br beside 73 Claflin St. US of grate |
| WIB012 | 1244 | Belmont | 0328 | 42 | 24 | 6.04 | 71 | 10 | 30.3 | centerline | Winn's Br on E side of Clifton St by Hickory Lane |
| WIB013 | 1245 | Belmont | 0328 | 42 | 24 | 6.33 | 71 | 10 | 36.42 | centerline | Winn's Br @ Howells Rd footpath bridge- park on Fletcher & walk up driveway of blue house |
| WIBUTB | 1246 | Belmont | 0328 | 42 | 24 | 14.50 | 71 | 10 | 36.13 | tributary | Tributary 'B' to Winn's Br on S side of Prospect St W of Clifton- park on Prentiss |
| WIB018 | 1247 | Belmont | 0328 | 42 | 24 | 11.74 | 71 | 10 | 54.39 | centerline | Winn's Br @ Juniper Rd |
| ATB007 | 1248 | Belmont | 0328 | 42 | 24 | 3.35 | 71 | 11 | 13.41 | centerline | Atkins Br @ Somerset St (near Habitat sanctuary) |
| WEB013 | 1249 | Belmont | 0328 | 42 | 23 | 42.89 | 71 | 10 | 34.74 | centerline | Wellington Brook emerging from under Common Street- park on Dunbarton Rd |
| WEB010 | 1250 | Belmont | 0328 | 42 | 23 | 39.4 | 71 | 10 | 19.02 | centerline | Wellington Brook behind E end of library where brook goes back underground |
| WEB007 | 1251 | Belmont | 0328 | 42 | 23 | 36.82 | 71 | 10 | 0.29 | centerline | Wellington Brook inflow to Claypit Pond @ SW corner by Concord Ave. |
| BEL08N | 1252 | Belmont | 0328 | 42 | 23 | 40.46 | 71 | 9 | 29.86 | pipe | North (& side) pipe of two circular pipes- inflow to Blair Pond where Wellington Br emerges fr Blanchard Rd/Brighton St |
| CAMD34 | 1253 | Cambridge | 0328 | 42 | 23 | 40.3 | 71 | 9 | 29.83 | pipe | South, rectangular outfall- inflow to Blair Pond where Wellington Br emerges fr Blanchard Rd/Brighton St |
| WEB002 | 1254 | Belmont/ Cambridge | 0328 | 42 | 23 | 43.80 | 71 | 9 | 23.45 | centerline | Blair Pond outlet on N side just before R/R- becomes Wellington Br.- park on Flanders Rd. |